## Slide 1
Confidential
IOT POC
Prepared For collecting telemetry data from industrial devices and sending data to Azure Digital Twin
Sep 2023
Tiger Analytics

## Slide 2
Use Case Overview
Industrial sensors, actuators and devices communicates with services or applications using various communication protocols. It includes both open source (such as Modbus TCP/RTU, ProfinNet IO etc) and vendor specific proprietary protocols (such as Siemens S7 ISOTCP, Mitsubishi 3E/1E/FX, Beckhoff ADS etc.).
First these protocol data must be converted into an acceptable message format so that it can be used for further data processing or storage using various applications. IoT applications generally accepts messages in MQTT format, so it is preferable to convert the industrial communication protocol data into a standard MQTT data format.
Some industrial process required fast action for example, if the temperature of the machine exceeds threshold value, it must be stopped immediately. For these applications it is preferable to do data analytics at the edge (close to the process) to reduce the latency.
The data collected near real time/over the period of a process has to be sent to the cloud for big data analytics and model building. The network connectivity will be unreliable if the factory is located in some remote location. The data has to be stored locally and resent once network connectivity resumes.
In cloud, the data should be stored in database for further processing, and near real time data should be displayed for gathering business insights.
The command from dashboards from cloud to device has to be passed to set operational parameters of the process.

## Slide 3
Solution Approach
The industrial protocol data first converted in to standard MQTT message format using Neuron. Neuron is an open source, Industrial IoT connectivity server that translate various industrial protocol data in to MQTT formatted data.
PeakHMI simulator is used to simulate the ModBus TCP data in this demo.
Ekuiper is used for edge data analytics. It is also an open source, stream processing and edge analytics engine. Ekuiper receives telemetry from Neuron and perform analytics using rule engine. Ekuiper supports both SQL query based and graph-based approach for creating rules.
In this demo, three rules are created,
                1. Check the parameter values at the edge, if it exceeds the threshold command will be issued back to the device.
                2. Send telemetry data to Azure IoT hub
                3. Get command from Azure IoT hub.
                Azure IoT hub receives the message from Ekuiper and pass the telemetry to other Azure services in the cloud. Two events are created in hub, one for storing data in to blob storage and another one for sending the data to azure function.
                Azure function receives the events from IoT hub whenever telemetry event occurs. It process the events and update the Azure digital twin.
                Models and relationships are created in the digital twin based on the relationship between actual process (in this demo two devices are connected to a process). The values will be updated whenever telemetry data received by IoT hub.
                Whenever a command is set in digital twin, the event will be triggered, the associated Azure function process the event, and update the desired property of device twin in IoT hub device. It will then pass on to device through Ekuiper and Neuron.

## Slide 4
Architecture Diagram
Modbus TCP/RTU
OPC UA
Profinet IO
EtherNet/IP, etc
Event hub
Azure Functions App
Ekuiper
Neuron
Azure Digital Twin
ADLS
Azure IoT hub
Azure Functions App
ADT patch
Communication protocols used in industrial devices
MQTT Msg
Edge
Cloud
Event hub
Device twin update

## Slide 5
Business Outcome
Existing industrial devices having different protocol connectivity can be easily interfaced to the cloud.
Seamless data flow from industrial devices to the cloud and vice versa.
Edge analytics can be performed close to the process. This will reduce the latency and improves the accuracy.
Digital twin that is digital equivalent of the actual process can be created, the near real time data and relationship among them will be displayed in dashboard.
Industrial devices can be monitored and controlled from cloud.
The devices data will be stored in cloud for further data processing and analytics.

## Slide 6
Challenges Faced
Neuron and Ekuiper installation on WSL
  Neuron and Ekuiper can be installed on both Linux based machines and WSL. If it is installed in WSL, make sure that “distrod” is
  installed before installing Neuron and Ekuiper. By default, WSL does not have “systemd” service installed, when above mentioned
  applications installed as container application using docker it will not start. Install “distrod” from this link and use option 2.
Telemetry data base64 encoded
While connecting Ekuiper with Azure IoT hub using MQTT protocol, add the following MQTT topic, the highlighted part will set the
application type and encoding, otherwise telemetry data will be base64 encoded.
“devices/IIoT_Modbus/messages/events/$.ct=application%2Fjson%3Bcharset%3Dutf-8“
Interfacing Ekuiper to Azure IoT hub
For receiving the desired property patch from device twin of device in IoT hub use the following topic,
“$iothub/twin/PATCH/properties/desired/#”
Digital twin telemetry data update
Provide “Azure digital twin data owner role” for the Azure function app to the digital twin, otherwise telemetry data will not be updated
(You won't get any error message).

## Slide 7
Demo
https://drive.google.com/file/d/1Qf-dqZjnuU1CfMLN8qUFS9J6a2vZOve1/view?usp=drive_link

## Slide 8
Resources
1. Demo link
https://drive.google.com/file/d/1Qf-dqZjnuU1CfMLN8qUFS9J6a2vZOve1/view?usp=drive_link
2. Documentation
https://docs.google.com/document/d/1SiOjqP-siE1n3rhlRSNS2Mzt7kYekvGATXzUiRcFZOE/edit?usp=sharing
3. Digital twin link
https://explorer.digitaltwins.azure.net/?tid=e714ef31-faab-41d2-9f1e-e6df4af16ab8&eid=iot-digital-twin-poc.api.wcus.digitaltwins.azure.net
4. IoT hub device link
https://portal.azure.com/#view/Microsoft_Azure_IotHub/IotHubDeviceFrameBlade/path/%2Fdevices%2Fdevice%3FdeviceId%3DIIoT_Modbus/title/IIoT_Modbus/resourceId/%2Fsubscriptions%2Fbbe310c3-28f6-426a-a962-d19168e0b958%2FresourceGroups%2Fvena-energy%2Fproviders%2FMicrosoft.Devices%2FIotHubs%2FESP32Experiment

## Slide 9
Thank You
Do you have any questions?